## Slide 1: XRN4645 - The rejection of incrementing reads submitted for an Isolated Supply Meter Point (RGMA flows) Change Details
High Level System Solution Impact Assessment

## Slide 2: Change Overview
XRN4645 - The rejection of incrementing reads submitted for an Isolated Supply Meter Point (RGMA flows) Change Details
Xoserve has received in excess of 7000 RGMA transactions where the User has provided a Meter Information Notification (JOB transaction) or Meter Information Update Notification (UPD transaction) to reverse an isolation of a Capped or Clamped Supply Meter Point but that the reading provided in the transaction has incremented from the reading provided at isolation. When a User indicates that the Supply Meter Point is isolated, they are indicating that it is not capable of flowing gas (UNC Section G 3.4), and therefore an incrementing reading is not expected following such isolation. Other reading processes reject any incrementing readings. Where a User submits an RGMA transaction to update the meter information the transaction is currently being processed, and the UK Link system is being updated with the Metering Information contained within the transaction. However, given that the User has informed the CDSP that the Supply Meter Point is not capable of flowing gas this has been excluded from allocation processes, and therefore any attempt to reconcile the Supply Meter Point creates an error within the invoicing process. As such these items are being currently excluded from the Amendment invoice. This is causing issues with the daily volume and energy calculated for reconciliation. A proportionate solution needs to be developed to support the ability for Users to retain the ability to notify where a Meter is not capable of passing gas (UNC Section G3.4) but reduce the risk to downstream processes and the wider industry.
Solution Options
1
New Rejection Code to be required to be applied for the rejection of incrementing read

## Slide 3: Option 1 - High Level Impact Assessment
1 - New Rejection Code to be required to be applied for the rejection of incrementing reads
This solution option is proposing a new rejection code for RGMA transactions where the supplied read indicates gas has been consumed on an isolated supply meter point. The new rejection code would apply to premises where the status of the meter/meter point indicates that the meter is no longer capable of flowing gas e.g. the meter is removed capped or clamped.
Assumptions
Performance Testing would not be required Market Trails would not be required New rejection code needed informing submitting parties of RGMA read indicating consumption on an isolated premise
Overall Impact | Release Type | High Level Cost Estimate
Medium | Major | 40,000 to 60,000 GBP
Impacted Systems
Marketflow
SAP PO
SAP ISU
Gemini
SAP BW
CMS
DES
API
Impact
1

## Slide 4
 | Reports | Interface | Conversion | Enhancements | Forms | Workflow | Data Migration
System Component: |  | PO/Marketflow |  |  |  |  | 
Impacted Process Areas: |  | RGMA |  |  |  |  | 
Complexity Level (per RICEFW item): |  | Low |  |  |  |  | 
Change Description: |  | Configuration of new rejection code on outbound RGMA response file(s) |  |  |  |  | 
 | ISU | BW | PO / Marketflow | DES | CMS | AMT | API
Test Data Prep Complexity: | Low |  | Low |  |  | Low | 
Unit and Sys Test Complexity: | Low |  | Low |  |  | Low | 
Pen Test Impact: | No |  | No |  |  | No | 
Regression Testing Coverage: | Low |  | Low |  |  | Low | 
Performance Test Impact: | No |  | No |  |  | No | 
Market Trials: | No |  | No |  |  | No | 
UAT Complexity: | Low |  | Low |  |  | Low | 
Option 1 - System Impact Assessment
1

## Slide 5
Process Area | Complexity | File Formats | Exceptions | External Screens | Batch Jobs | Performance Test?
SPA | n/a | n/a | n/a | n/a | n/a | n/a
Metering (Reads) | n/a | n/a | n/a | n/a | n/a | n/a
Reconciliation | n/a | n/a | n/a | n/a | n/a | n/a
Invoicing - Capacity | n/a | n/a | n/a | n/a | n/a | n/a
Invoicing – Commodity | n/a | n/a | n/a | n/a | n/a | n/a
Invoicing - Amendment | n/a | n/a | n/a | n/a | n/a | n/a
Invoicing - Other | n/a | n/a | n/a | n/a | n/a | n/a
Rolling AQ | n/a | n/a | n/a | n/a | n/a | n/a
Formula Year AQ | n/a | n/a | n/a | n/a | n/a | n/a
RGMA | Low | Yes | No | No | No | No
DSC Service | n/a | n/a | n/a | n/a | n/a | n/a
Other (Specify) | n/a | n/a | n/a | n/a | n/a | n/a
Option 1 - Process Impact Assessment
1